## Slide 1
Digital Communication 24EC2208
Pulse Modulation Systems

## Slide 2: Outlines
Introduction
PAM
PWM
PPM
Comparison

## Slide 3: Introduction
AM, FM and PM : Continuous Carrier wave,
Frequency translation.
Pulse Modulation: Pulse carrier wave, short distance.
Pulse Modulated waves are rich in d.c and low frequency components.
Direct transmission of Pulse modulated signal is very difficult.

## Slide 6: Pulse Amplitude Modulation

## Slide 7
Sampling Process

## Slide 9: Pulse Amplitude Modulation
PAM may be defined as the type of modulation in which the amplitudes of regularly spaced rectangular pulses vary according to the instantaneous value of the modulating signal.
The pulses of PAM signal may be flat type or natural type.
PAM is two step process.
Instantaneous
Sampling
2. Lengthening

## Slide 10
Instantaneous
Sampling
2. Lengthening

## Slide 11: PAM Generation

## Slide 12: PAM Demodulation
Equalizer: Compensate for magnitude distortion and phase delay
Reconstruction Filter: LPF

## Slide 13: Equalizer
The equalizer has the effect of decreasing the in-band loss of the reconstruction filter as the frequency increases in such a manner as to compensate for the aperture effect.
Designed with acoustics in mind, to “equalize” all of the sound frequencies.

## Slide 15: Advantages of PAM
It is the base for all digital modulation techniques and it is simple process for both modulation and demodulation technique.
No complex circuitry is required for both transmission and reception. Transmitter and receiver circuitry is simple and easy to construct.
PAM can generate other pulse modulation signals and can carry the message or information at same time.

## Slide 16: Dis-advantages of PAM
Bandwidth is high.
Since the noise affects the amplitude of the waveform, like AM, PAM is also less immune to noise.
PAM waveform has pulses with varying amplitude and therefore power required to transmit them is not constant. This requires that the transmitter must be able to handle the power required to transmit pulse having maximum amplitude.

## Slide 17: Sample and Hold

## Slide 18
The sample and hold circuit generates the samples of the analogue input signal and holds the latest sampled values for definite time and reflects it at the output.

## Slide 20
Application of Sample and Hold Circuit
Data Distribution System
Sampling Oscilloscopes
Data Conversion System
Digital Voltmeters
Analog Signal Processing
Signal Constructional Filters

## Slide 21: Pulse Time Modulation

## Slide 22: Pulse Time Modulation

## Slide 23: Pulse Width Modulation Pulse Duration Modulation Pulse Length Modulation

## Slide 24
Pulse Train

## Slide 25: Pulse Width Modulation
In PWM, the width of the carrier pulses is varied in accordance with the modulating signal
Direct Method

## Slide 26: Indirect Method of PWM
Spectrum of PWM

## Slide 27: Demodulation of PWM

## Slide 28: PWM Demodulator

## Slide 29: Pulse Position Modulation (PPM)

## Slide 30
PPM

## Slide 31: PPM Demodulation

## Slide 32: Comparison

## Slide 33: End