## Slide 1: Digital Communication
Matched Filter

## Slide 2: Baseband Pulse Transmission Matched Filter
The term base-band is used to designate the band of frequencies representing the original signal delivered by a source of information

## Slide 4: Binary Base-band data transmission System
The term base-band is used to designate the band of frequencies representing the original signal delivered by a source of information

## Slide 5
Block diagram of a baseband binary transceiver

## Slide 6: Introduction to Matched Filter
The transmission of digital data over a baseband channel is affected by channel noise as illustrated below:
A basic problem that often arises in the study of communication systems is that of detecting a pulse transmitted over a channel that is corrupted by channel noise.
A device (an LTI filter) for optimum detection of a pulse corrupted by noise in the channel is referred to as Matched filter.
i.e.,the impulse response of the Matched filter is matched to the pulse signal.

## Slide 7: Matched Filter
A matched filter is a linear filter designed to provide the maximum signal-to-noise power ratio at its output. This is very often used at the receiver.
Receiver Model

## Slide 8
Consider that the filter input x(t) consists of a pulse signal g(t) corrupted by additive noise w(t) .
It is assumed that the receiver has knowledge of the waveform of the pulse signal g(t).
The source of uncertainty lies in the noise w(t).
The function of receiver is to detect the pulse signal g(t) in an optimum manner, given the received signal x(t).
The purpose of the circuit is to design an impulse response h(t) of the filter such that the output signal-to-noise ratio is maximized.

## Slide 13: Properties of Matched Filter
Property1. A filter matched to a pulse signal g(t) of duration T is characterized by an impulse response that is time-reversed and delayed version of the input g(t):
Property2. A matched filter is uniquely defined by the waveform of the pulse but for the:
- time delay T
- Scaling factor k
Property3: The peak signal-to-noise ratio of the matched filter depends only on the ratio of the signal energy to the power spectral density of the white noise at the filter input.

## Slide 14: End