## Slide 1: Digital Communication
Inter Symbol Interference

## Slide 2: Binary Base-band data transmission System

## Slide 3
The transmission of digital data over a baseband channel
Digital data have a broad spectrum with a significant low-frequency content.
Baseband transmission of digital data therefore requires the use of a low-pass channel with a bandwidth large enough to accommodate the essential frequency content of the data stream.
Typically, however, the channel is dispersive in that its frequency response deviates from that of an ideal low-pass filter.
The result of data transmission over such a channel is that each received pulse is affected somewhat by adjacent pulses, thereby giving rise to a common form of interference called inter Symbol interference (ISI).
Inter symbol interference is a major source of bit errors in the reconstrcted data stream at the receiver. To correct for it, control has to be exercised over the pulse shape in the overall system.

## Slide 4: Inter Symbol Interference
Inter Symbol interference (ISI) occurs when a pulse spreads out in such a way that it interferes with adjacent pulses at the sample instant.
Example: assume polar NRZ line code. The channel outputs are shown as spreaded (width Tb becomes 2Tb) pulses shown (Spreading due to bandlimited channel characteristics).
Channel Output
Pulse width Tb
Data 1
Data 0
Channel Input Pulse width Tb

## Slide 5
ISI
If the rectangular multilevel pulses are filtered improperly as they pass through a communications system, they will spread in time, and the pulse for each symbol may be smeared into adjacent time slots and cause Intersymbol Interference.
How can we restrict BW and at the same time not introduce ISI? 3 Techniques.

## Slide 6: Intersymbol Interference
For the input data stream:
The channel output is the superposition of each bit’s output:
1
1
1
1
0
0
1
1
1
1
0
0
Resultant Channel Output Waveform

## Slide 7: Inter Symbol Interference
Inter Symbol Interference (ISI) is caused by nonideal channels that are distorted over the entire input signal bandwidth. ISI, as a manifestation of channel distortion, can cause errors in pulse detection if it is large enough.

## Slide 10: ISI elimination techniques
It is important to note that pulse amplitudes can be detected correctly despite pulse spreading (or overlapping), if there is no ISI at the decision-making instants.
This can be accomplished by a properly shaped band limited pulse signals.
To eliminate the effect of ISI, Nyquist proposed the following criteria for pulse shaping.
Ideal Nyquist Criterion: Sinc Pulse.
Practical filter: Raised Cosine Filter

## Slide 11: End