## Slide 1: 1. For a transmission line which is terminated in a normalized impedance Zn, VSWR = 2. Then calculate the normalized impedance magnitude.

## Slide 2: 2. A lossless transmission line used in a TV receiver has a capacitance of 50pf/m and an inductance of 200 nH/m. Then calculate the characteristic impedance for the sections of a line 10 mete long and 500 meter long.

## Slide 4: 3. A lossless transmission line is terminated in a load impedance of 30-j23 ohms. Then by applying the concept of infinite line calculate the phase constant and the reflection coefficient of a line of length 50m, with characteristic impedance 50ohms and wavelength on the line is 0.45m.

## Slide 5: 4. A lossy cable which has R =2.25 ohms/m, L=1 micro H /m, C= 1 peco F /m, and G=0 operates at a frequency of 0.5GHz. Then analyze the scenario and calculate attenuation constant of the line.

## Slide 6: 5. A two-wire open air line, whose diameter is 2.588mm is used in several applications. The wires are spaced at 290mm between the centers. Then calculate the characteristic impedance of the line.

## Slide 7: 6. A transmission line is lossless and is 25m long. It is terminated in a load of 40+j30 ohms at a frequency of 10MHz. The inductance and capacitance of the line are L =300nH/m, C=40pF/m. Then calculate the input impedance at the source and at the midpoint of the line.