## Slide 1: Digital Communication 22EC2208
Dr. M. Venu Gopala Rao
A.M.I.E.T.E, M.Tech, Ph.D(Engg)
Cert. in R.S.T ( City & Guild’s London Institute, London)
F.I.E.T.E, L.M.I.S.T.E, I.S.O.I., S.S.I., M.I.A.E.
Professor, Dept. of ECE, K L University
mvgr03@kluniversity.in
Pulse Code Modulation

## Slide 6: Advantages of Digital Transmission
The primary advantage of digital transmission over analog transmission is noise immunity.
Digital signals are inherently less susceptible than analog signals to interference caused by noise, because with digital signals it is not necessary to evaluate the precise amplitude, frequency, or phase to ascertain its logic condition.
Instead, pulses are evaluated during a precise time interval, and a simple determination is made whether the pulse is above or below a prescribed reference level.

## Slide 7
Digital communication systems are cheaper to implement, because of the advancement of VLSI technology.
Digital signals are better suited than analog signals for processing and combining using a technique called multiplexing.
It is much simpler to store digital signals than analog signals, and the transmission rate of digital signals can be easily changed to adapt to different environments and to interface with different types of equipment.
Digital transmission systems are more resistant to analog systems to additive noise because they use signal regeneration rather than signal amplification.
digital regenerators sample noisy signals and then reproduce an entirely new digital signal with the same signal-to-noise ratio as the original transmitted signal. Therefore, digital signals can be transported longer distances than analog signals.

## Slide 8: Regeneration of PCM signal

## Slide 9
Digital signals are simpler to measure and evaluate than analog signals. Therefore, it is easier to compare the error performance of one digital system to another digital system.
Also, with digital signals, transmission errors can be detected and corrected more easily and more accurately than is possible with analog signals
Disadvantages of Digital Transmission
The transmission of digitally encoded analog signals requires significantly more bandwidth than simply transmitting the original analog signal.
ADC and DAC are needed
Requires precise time synchronization between the clocks in the transmitters and receivers
Digital transmission systems are incompatible with older analog transmission systems

## Slide 10: Pulse Code Modulation
Pulse code modulation (PCM) is a digital transmission system with analog to digital converter (ADC) at the input and a digital to analog converter (DAC) at the output.

## Slide 11: Practical Sampling Rates
Speech
- Telephone quality speech has a bandwidth of 4 kHz (actually 300 to 3300Hz)
- Most digital telephone systems are sampled at 8000 samples/sec
Audio:
- The highest frequency the human ear can hear is approximately 15kHz
- CD quality audio are sampled at rate of 44,100 samples/sec
Video
- The human eye requires samples at a rate of at least 20 frames/sec to achieve smooth motion

## Slide 12: Regeneration of PCM signal

## Slide 13: A PCM System
DT sequence

## Slide 14: Examples of PCM

## Slide 15: Sampling
x[n] = {1.3, 3.6, 2.3, 0.7, -0.7, -2.4, -3.4 }

## Slide 17: Quantization and Encoding

## Slide 18
Sampling, Quantization and Encoding

## Slide 19: Uniform Quantization

## Slide 21: Quantization and Encoding

## Slide 22
Assigning PCM codes to absolute magnitudes is called Quantizing.
The magnitude difference between adjacent step is called the quantization interval / quantum.
The magnitude of the quantum is also called the resolution.
The resolution is equal to the voltage of the minimum step size = Voltage of LSB.

## Slide 23: Midtread and Midrise Quantizer Characteristics

## Slide 25
Quantization Error

## Slide 26
Ex1: Quantize a sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3} using a uniform quantizer in the range of (-1.5. 1.5) with (i) Four levels (ii) Eight levels, and write the quantized sequences. Determine the quantization error in each case. Write the encoded sequence. Find the full scale accuracy. Find the percentage accuracy.
The full scale accuracy
The percentage accuracy

## Slide 27
1.125
0.125
1.125
0.375
-0.375
-0.375
Given Sequence
{1.2, -0.2, -0.5, 0.4, 0.89, 1.3}
Bit stream representing Encoding: 11 01 01 10 11 11
00
01
10
11

## Slide 28
Ex1: Quantize a sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3} using a uniform quantizer in the range of (-1.5. 1.5) with (i) Four levels (ii) Eight levels, and write the quantized sequences. Determine the quantization error in each case. Write the encoded sequence
(i) For L = 4;
Therefore the quantization error
codewords 00 01 10 11
Quantization levels = { -1.5, -1.125, -0.75, -0.375, 0, 0.375, 0.75, 1.125, 1.5 }
Given Sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3}
Therefore the quantized sequence {1.125, -0.375, -0.375, 0.375, 0.125, 1.125}
Bit stream representing Encoding: 11 01 01 10 11 11

## Slide 29: Bandwidth of PCM

## Slide 30: Bandwidth of PCM…

## Slide 31: Formulas

## Slide 32
Ex: Consider a 12 bit uniform quantizer with input range of Volts.
Calculate the step size and maximum quantization error.
Therefore maximum quantization error

## Slide 38
Sampling rate 200Hz
Min.bit rate = (No.of bits)*(sampling rate) = 14*200 = 2800 bits/sec

## Slide 40: Noise consideration in PCM system
The performance of a PCM system is influenced by two major sources of noise.
Channel noise: which is introduced anywhere between the transmitter output and the receiver input, channel noise is always present, once the equipment is switched on.
2. Quantization noise, which is introduced in the transmitter
and is carried all the way along to the receiver output.

## Slide 41: Quantization Error and Noise Power

## Slide 42: Signal to Quantization Noise Ratio

## Slide 43
6 dB rule

## Slide 44
Case1:

## Slide 45
Case2:

## Slide 46
Case3:
Case4:

## Slide 47
(i) Signal Power
Noise Power

## Slide 48
(ii)

## Slide 49
Ex: In a binary PCM system, the output SQNR is to be held to a minimum of 40 dB. Determine the of required levels, and find the corresponding output SQNR.
Ans:

## Slide 50
Ex1: Quantize a sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3} using a uniform quantizer in the range of (-1.5. 1.5) with (i) Four levels (ii) Eight levels, and write the quantized sequences. Determine the quantization error in each case. Write the encoded sequence. Find the full scale accuracy. Find the percentage accuracy

## Slide 51
1.125
0.125
1.125
0.375
-0.375
-0.375
Given Sequence
{1.2, -0.2, -0.5, 0.4, 0.89, 1.3}
Bit stream representing Encoding: 11 01 01 10 11 11
00
01
10
01

## Slide 52
Ex1: Quantize a sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3} using a uniform quantizer in the range of (-1.5. 1.5) with (i) Four levels (ii) Eight levels, and write the quantized sequences. Determine the quantization error in each case. Write the encoded sequence
(i) For L = 4;
Therefore the quantization error
codewords 00 01 10 11
Quantization levels = { -1.5, -1.125, -0.75, -0.375, 0, 0.375, 0.75, 1.125, 1.5 }
Given Sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3}
Therefore the quantized sequence {1.125, -0.375, -0.375, 0.375, 0.125, 1.125}
Bit stream representing Encoding: 11 01 01 10 11 11

## Slide 53
(ii) L = 8.
Therefore the quantization error
Quantization levels = { -1.5, -1.3125, -1.125, -0.9375, -0.75, -0.5625, -0.375, 0, 0.375, 0.5625, 0.75, 0.9375, 1.125, 1.3125, 1.5 }
Given Sequence {1.2, -0.2, -0.5. 0.4, 0.89, 1.3}
Therefore the quantized sequence
{1.3125, -0.1875, -0.5625, 0.5625, 0.9375, 1.3125}

## Slide 55: End